## Slide 1: Hands-on
discuss SPGs of aquatic invertebrates
discuss available DLT simulation outcome
Do analysis, outcome
  Material: HDF arr.dat, HDF viewer, Jupyter Notebook

## Slide 2: Hands-on
Case Study | Regulatory Framework of Higher-tier Landscape-level Aquatic Risk Assessment in Europe

## Slide 3: xLandscape Case Study Context: Aquatic Risk Assessment
Risk of aquatic invertebrates due to insecticide use in arable crops.
A classical use of Landscape Modelling!
Notes: introduce and emphasise the use of xAquaticRisk in the classical RA context (EU, aquatic guidance document, SPGs.

## Slide 4: Problem Formulation: lower Tier indicated risk
Key environmental concern is the very high toxicity to aquatic invertebrates
We assume a Regulatory Acceptable Concentration of RAC ~ 1 ng/L
If exposure, PECsw ≤ RAC ⇒ Risk acceptable
Our CaseStudy 'SynPyrethroid' is used in arable crops, at an application rate of 1x 7.5 g a.s./ha
Standard, edge-of-the-field exposure assessment results in PECsw_FOCUS ~ 2 ng/L unaccepable risk
Pyrethrum is known as insect pest control since antiquity (Persian insect powder). Synthetic derivatives, pyrethroids, appeared in the 1970s, which overcome photoinstability of natural ancestors and which toxicity is selective to arthropods (SupportingDocs).
There is a high demand for phyrethroid pest and vector control (eg, cicada Philaenus spumarius spreading Xylella fastidiosa, killing olive trees). Pyrethroid pesticides are authorised in many crops (eg, cereals, oilseed, soybeans, fruit, olives, cotton, vegetables, rice), in countries across the world.
FOCUS Surface Water Scenarios (2001) SANCO/4802/2001 rev. 2; FOCUS Surface Water (2015) Generic guidance v 1.4
FOCUSsw approach
Objectives Higher-Tier Risk Assessment for Aquatic Invertebrates
Make exposure assessment more realistic. Design approach guided by Specific Protection Goals.
Link effect to exposure modelling. Identify effective risk management measures. Support weight-of-evidence assessment.
Responsibility and Innovation: increase knowledge on real-world exposure and effects, also for next generation of approaches.
Notes: this case study represent THE classical use of landscape modelling in risk assessment of pesticides . emphasise and highlight the key terms that characterises a higher-tier RA. suggest to participant to get deeper into the topic. Innovation and responsibility

## Slide 5: Questions, Discussion Points
Why move to higher-tier/Tier4? FOCUS gives ~2 ng/L while the RAC is ~1 ng/L (unacceptable at lower tier). What exactly would you need to see (data or model evidence) to justify moving to a Tier‑4 landscape approach—and what would count as “more realistic” in this case?
SPGs as the steering wheelWhich SPG “dimension” is most decisive for choosing endpoints in this training—entity, attribute, magnitude, temporal scale, spatial scale, or certainty—and why? (Pick one and defend it.)
ETO vs ERO (threshold vs recovery). Which extra efforts will the ERO bring to higher-tier landscape modelling approach for an insecticide. For pyrethroids and aquatic invertebrates, when would you argue for an Ecological Threshold Option (ETO) versus an Ecological Recovery Option (ERO)? What kind of evidence would you consider “strong enough” to support ERO?
What changes from FOCUS → Tier‑4 (and what doesn’t)?What is fundamentally different when going from a Step 3/4-style exposure–RAC comparison to a Tier‑4 landscape coupling of exposure and effects—and what conservative assumptions may still remain even at Tier‑4?
The “ensemble” idea (protecting the system, not every ditch)The slides argue for protecting an ensemble of edge‑of‑field waters rather than each single segment. How would you explain (to a regulator or stakeholder) why that is still protective—and where you would draw the line for unacceptable hotspots?
Endpoints & percentiles: what do they mean in practice?When you see “spatial percentiles” and “temporal percentiles” of PECsw(x,t), what real-world protection statement are you making? Which percentile combination feels defensible for decision-making—and why?
Exposure framing choice: “Exposed-only streams”What changes (conceptually and numerically) when you switch to an “exposed-only streams” analysis? In which regulatory contexts could this be justified, and where could it be misleading?
Mitigation: from simulation result → practical ruleThe mitigation example (buffer + drift reduction) shows large reductions. How would you translate that into a simple, auditable risk‑management rule (e.g., targeted hotspots vs blanket mitigation), and what extra information would you need?
Optional “hands-on starter” (quick warm-up question)If you want a 60‑second opener before the notebook work:What would you expect to be the biggest practical bottleneck today: understanding SPGs, finding/QA’ing parameterisation data, running the simulation workflow, or interpreting output percentiles?

## Slide 6: Questions, Discussion Points
1. Why move to Tier‑4?
  FOCUS gives PECsw ≈ 2 ng/L while RAC ≈ 1 ng/L. What *specific* evidence would justify a Tier‑4 landscape approach—and what does “more realistic” mean here?
2. SPGs as the steering wheel**
Which SPG dimension most strongly drives endpoint choice in this case (entity, magnitude, spatial scale, temporal scale, certainty)? Why?
**3. Threshold or recovery? (ETO vs ERO)**
For pyrethroids and aquatic invertebrates, when would ERO be defensible—and what evidence would regulators need to see?
**4. What really changes at Tier‑4?**
Compared to FOCUS Step 3/4, what is fundamentally different when exposure and effects are *coupled* at landscape scale—and which conservative assumptions still remain?
**5. Protecting an “ensemble”, not every ditch**
How would you explain to a regulator why protecting an ensemble of edge‑of‑field waters is still protective? Where do unacceptable hotspots begin?
**6. Percentiles = protection statements**
What real‑world protection claim do spatial and temporal PECsw percentiles make? Which percentile combination feels defensible for decisions?
**7. “Exposed‑only streams” framing**
What changes conceptually and numerically when analysing only exposed stream segments—and when could this be misleading?
**8. From model output to mitigation rule**
How would you translate the mitigation results into a simple, auditable risk‑management rule (hotspot‑targeted vs blanket)?
### *(Optional speaker notes – keep hidden)*
* These questions mirror the **story arc of the training**: problem formulation → SPGs → Tier‑4 design → endpoints → mitigation.
* There are **no single correct answers**; the goal is to surface assumptions and trade‑offs.
* Encourage participants to answer **as if they were the risk assessor**, not the modeller.
* If time is short: use **Q1, Q3, and Q6** as a minimal set.

## Slide 7: Supplement Regulatory Acceptable Concentration (RAC)
The Regulatory Acceptable Concentration (RAC) is the maximum concentration of a pesticide in the environment that is considered safe for non‑target organisms. At Tier 1 (standard lab tests), the RAC is usually:
Typical steps:
Select endpoint: Acute: LC50/EC50 for fish, invertebrates, algae, macrophytes. Chronic: NOEC/EC10 for sensitive taxa.
Choose the most sensitive relevant endpoint: Often the lowest chronic NOEC/EC10 across taxa is used for long‑term RACsw.
Assessment factor (AF). Applied to account for uncertainty: 10 for strong chronic datasets, 50–100 for acute data
Higher‑tier options (SSD and mesocosms): When Tier‑1 is too conservative or fails, EFSA’s aquatic guidance allows refinement
Species Sensitivity Distributions (SSD): Use multiple chronic endpoints (e.g. EC10/NOEC for many species). Fit an SSD and derive an HC5 (hazard concentration for 5% of species). Apply a smaller AF (e.g. 1–5) to HC5 → refined RAC.
Micro‑/mesocosm studies (model ecosystems): Expose realistic aquatic communities to the pesticide. Identify the highest concentration with negligible or acceptable population‑level effects, depending on the protection goal. This concentration (possibly with a small AF) becomes the RAC
ETO vs ERO (protection goal choice). EFSA distinguishes two protection goal options for deriving RACs from higher‑tier data:
  Ecological Threshold Option (ETO): Only negligible effects at population level are allowed. RAC is set at the highest concentration with no or only minor, transient effects.
  Ecological Recovery Option (ERO): Some initial population‑level effects are allowed if recovery occurs within an acceptable time (e.g. within weeks). RAC can be higher than the ETO‑RAC, but must be justified by clear recovery in the mesocosm data.
Once the aquatic RACsurfacewater/sediment is set, it is compared with modelled or measured exposure: eg, PECsw ≤ RACsw  aquatic risk acceptable
If the risk is not acceptable, regulators may require risk mitigation (eg, buffer zones, drift‑reducing nozzles, reduced application rates) or they may reject the product.
At lower (standard) tiers, PECsw/sed are calculated using the FOCUSsw approach, at higher-tier landscape models and scenarios come in, eg, xAquaticRisk

## Slide 8: why can we do that?! Tiered Aquatic Risk Assessment (EU)
Regulation EC 1107/2009, Data Requirements, Uniform Principles, Aquatic Guidance Document, Sustainable Use Directive, EFSA Scientific Opinions on Specific Protection Goals, PPR Panel scientific opinions on recovery in aquatic organisms/ecological threshold concepts, EFSA/PPR opinions and guidance on TKTD, EFSA uncertainty + weight-of-evidence guidance, FOCUS Surface Water, …
*SPG=Specific Protection Goal
Same protection goal at all tiers
Key: Higher-Tier Approach guided by Specific Protection Goals. Supporting evidence.
Assessment: acceptable effects? Quantify Exposure and Effects in Dimensions and Scales defined in SPGs

## Slide 9: Supplement Risk
MODULE | Regulatory Framework of Higher-tier Landscape-level Aquatic Risk Assessment in Europe


## Slide 10: Supplement Regulations framing higher-tier risk assessment
MODULE | Regulatory Framework of Higher-tier Landscape-level Aquatic Risk Assessment in Europe


## Slide 11: Supplement Specific Protection Goals

## Slide 12: Supplement TKTD, GUTS

## Slide 13: how to make an appropriate Tier-4 modelling – how to design ‚more realistic‘?!
what drives the aquatic exposure for SynPyrethroid

## Slide 14: which variability do we address
modelling variability
‚resolve‘ variability
Monte Carlo

## Slide 15: The Modelling Approach xAquaticRisk
Spatiotemporally explicit Modeling Framework Interfaces ▪ Control ▪ MonteCarlo ▪ Dimensions ▪ Scales ▪ Semantics
Crop cultivation
Ag/Land.Mgmt
PPP use
Analysis
LP50
Population
Exposure
Effect
GUTS
MASTEP
StreamCom
xDrift
xRunoff
xDrainage
Exposure/Efate
Toxswa
Steps1234
Environment
Water temperature
Hydrology
Stream Network
CVASI
(https://github.com/xlandscape/xAquaticRisk)
Modular
Open Source, FAIR
Makes use of regulatory established models
Flexible, adaptable

## Slide 16: The Modelling Approach xAquaticRisk
Spatiotemporally explicit Modeling Framework Interfaces ▪ Control ▪ MonteCarlo ▪ Dimensions ▪ Scales ▪ Semantics
Crop cultivation
PPP use
LP50
Population
Exposure
xDrift
xRunoff
xDrainage
Toxswa
Steps1234
Water temperature
Hydrology
Stream Network
GUTS
MASTEP
StreamCom
CVASI
(https://github.com/xlandscape/xAquaticRisk)
Modular
Open Source, FAIR
Makes use of regulatory established models
Flexible, adaptable

## Slide 17: The Modelling Approach xAquaticRisk
(https://github.com/xlandscape/xAquaticRisk)
Modular
Open Source, FAIR
Makes use of regulatory established models
Flexible, adaptable, integrated
User get in touch with a single model

## Slide 18: Get xAquaticRisk no installation needed
xAquaticRisk.zip Github
download or clone from

## Slide 19: Parameterisation
Configuration – mc-xml
Parameterisation (.xrun, .yaml)
User Interface - WebUI

## Slide 20: Start a Simulation
Drag and Drop
your …xrun file
onto the
__start__.bat

## Slide 21: Advanced your IDE as xLandscape Operation Center
Visual Sudio Code (example)
Git, development, modelling, analysis, documentation
..all AI-suported

## Slide 22: Scenario – Wetterau
ModuleScenario development
show the Wetterau and the upper subcatchment ‚Münster‘

## Slide 23: Concepts for Landscape-scale Aquatic RA / SPGs as Basis
Basis: Specific Protection Goals (SPGs) for aquatic invertebrates, Aquatic Guidance, TKTD GD, …
  EFSA defines (SPGs) for aquatic invertebrates by linking ecological functions (below) to population-level endpoints:
  Entity to protect: Populations of aquatic invertebrates (not individuals)
  Attribute to protect: Abundance and structure (e.g. species composition)
  Magnitude of effect: either negligible (Ecological Threshold Option, ETO) or recoverable (Ecological Recovery Option, ERO)
  Temporal scale: Recovery within a defined time frame (e.g. 8 weeks)
  Spatial scale: Edge-of-field surface waters (e.g. ditches, ponds, streams)
SPGs are based on key roles of aquatic invertebrates in surface water:
  Decomposition and nutrient cycling
  Food web support (e.g. prey for fish and amphibians)
  Water quality regulation
  "Protecting populations ensures these functions remain intact even if some individuals are affected" (EFSA)

## Slide 24: Concepts for Landscape-scale Aquatic RA / Design
Design of Tier-4, landscape-scale exposure and effect assessment:
General: Tier-4 = higher-tier, dh introduce more reality (land use, landscape structure, exposure-source to aquatic system relationship, exposure-driving factors (eg wind), habitat quality, species occurrence, efate…)
Natural catchment as basis (='statistical population', by natural watersheds, no artificial delineation) Protection of the entirety (an ensemble) of edge-of-field water bodies, NOT each and every single one, dh NOT 100% of individual segements effects in local hotspots might occur. Otherwise, a single ditch, of 1cm water level, receiving significant spray-drift would drive the quatic RA of hundrets of km of streams
Conservative elements: Although more realistic, even a landscape-scale RA is a model system and still contains a number of conservative assumptions, eg,
  100% product use (DLT) in all crops given by the potential label, dh essentially on 100% of fields
  No spray-drift filtering by riparian vegetation (still 'filter-paper' spray-drift deposition scenario).
  No dyring-out of small ditches. This causes (artificially?) high peak PECsw, eg, at 1cm minimum water level
  100% of sensitive organisms exposed (no spatial heterogeneity in stream system). 100% occurrence of sensitive species
  …
'we bring the (conservative) ecotox story into the landscape' (eg sensitive species)

## Slide 25: Concepts for Landscape-scale Aquatic RA / Summary
Tier-4 Landscape-level aquatic RA
Exposure
TER/RQ
Effect
Individual-level
Effect
Population-level
PECsw percentiles
RAC
Tier-2c at catchment-level
Abundance
Safety margins (Multiplication factors)
LP50 percentiles
Recovery (in-/extrinsic)
TER/RQ
Discussion by stream types
Framing Context Information, eg, Region, Safety Margins, Species Occurrence, Field Obs.
core RA
accompanying RA